## Slide 1
Islamic University of Technology
Course no: Phy 4143
Course Title: Physics II
Course Teacher : Dr Md. Sahab Uddin
Professor

## Slide 2: Superposition theorem
Statement: According to this theorem, if there are number of voltage and current sources acting simultaneously in a network then each source can be treated as if it acts independently of the others. Hence we can calculate effect of one source at a time then superimpose i.e. algebraically add the effects of all the sources.
Step 1: First all the sources except one under consideration are removed. While removing these voltage sources their internal resistance are left behind, while removing the current sources, as their internal resistance is infinite they are replaced by an open circuit.
Step 2: Next current in the various branches and voltage across various branches due to single source is calculated.
Step 3: The process is repeated for other sources taken one at a time.
Step 4: Finally algebraic sum of currents and voltage drop across the resistors due to different sources is calculated.

## Slide 3
Step 1 : When V1 is operated and V2 is short circuited
Let I1 is the total current through the network when V1 is operated alone.
I1’ and I2’ are the loop currents in the loops 1 and 2 respectively as shown in the figure.
Then I1= I1’ + I2’
Apply KVL for loop 1: I1’ R1+ (I1’ + I2’ )R3 = V1
Or I1’ (R1+ R3) + I2’ R3 = V1 ..(1)
Apply KVL for loop 2: I2’ R2+ (I1’ + I2’ )R3 = 0
Or I1’ R3 + I2’(R2 +R3) = 0 ..(2)
Solving simultaneous equations 1 & 2, I1’ and I2’ can be calculated and hence I1 = I1’ + I2’ can be calculated.
Explanation

## Slide 4
Step 2: When V2 is operated and V1 is short circuited
Let I2 is the total current through the network when V2 is operated alone.
I1” and I2” are the loop currents in the loops 1 and 2 respectively as shown in the figure.
Then I2= I1” + I2”
Apply KVL for loop 1: I1” R1+ (I1” + I2” )R3 = 0
Or I1” (R1+ R3) + I2” R3 = 0 ..(3)
Apply KVL for loop 2: I2” R2+ (I1” + I2” )R3 = V2
Or I1” R3 + I2” (R2 +R3) = V2 ..(4)
Solving simultaneous equations 3 & 4 I1” and I2” can be calculated and hence I2 = I1” + I2” can be calculated
Finally algebraic sum of currents I1 and I2 due to sources V1 and V2 is calculated

## Slide 5: Problem-1
Using superposition theorem find the voltage across 10𝛺 resistor
Step 1 :, we keep only voltage source active
and the current source is removed and replaced by open branch.
So the circuit will become as shown in the figure.
current through R2 is
I1 =
=
A

## Slide 6
Step 2 :, we keep only current source active and the voltage source is removed and replaced by a short.
So the circuit will become as shown in the below figure.
Current through R2 is I2 = A
According to superposition theorem the total current through load R2 is the algebraic sum of I1 & I2
I= I1 + I2= A
Hence voltage across 10𝛺 is = I R2 =

## Slide 7: Problem-2
Using superposition theorem find the voltage across 2𝛺 resistor
Step 1: only the 28-volt battery is active and 7 volt battery is replaced by a short
Current through R2=I1=
I =
Current through R2 = I1= =

## Slide 8
Step 2: only the7-volt battery is active and 28 volt battery is replaced by a short
Current through R2 = I2=
I=
Current through R2= =
Hence the total current through R2 is 2+2=4A and
Voltage drop across R2 = current through R2 R2 = 4 8V

## Slide 9
Example1: Determine the current in each branch of the network using superposition theorem

## Slide 10
Example 2: Determine the current in each branch of the network using superposition theorem