## Slide 1
Islamic University of Technology
Course no: Phy 4143
Course Title: Physics II
Course Teacher : Dr Md. Sahab Uddin
Professor

## Slide 2
Norton’s Theorem
Norton’s theorem states that a linear two-terminal circuit can be replaced by an equivalent circuit consisting of a current source IN in parallel with a resistor RN, where IN is the short-circuit current through the terminals and RN is the input or equivalent resistance at the terminals when the independent sources are turned off.

## Slide 3
Norton’s Theorem

## Slide 4
Norton’s Theorem

## Slide 5
Norton’s Theorem Procedure
EXAMPLE 1: Find the Norton’s equivalent circuit. Then find the current through RL for the circuit of figure.
Norton’s Theorem

## Slide 6
Step 1:- Remove that portion of the network where the Norton’s equivalent circuit is found. In Figure below, this requires that the load resistor RL be temporarily removed from the network.
Norton’s Theorem
EXAMPLE 1: Find the Norton’s equivalent circuit. Then find the current through RL for the circuit of figure.
Norton’s Theorem Procedure

## Slide 7
Norton’s Theorem
EXAMPLE 1: Find the Norton’s equivalent circuit. Then find the current through RL for the circuit of figure.
Step 1:- Remove that portion of the network where the Norton’s equivalent circuit is found. In Figure below, this requires that the load resistor RL be temporarily removed from the network.
Norton’s Theorem Procedure

## Slide 8
Step 2:- Mark the terminals of the remaining two-terminal network. (The importance of this step will become obvious as we progress through some complex networks.)
Norton’s Theorem
EXAMPLE 1: Find the Norton’s equivalent circuit. Then find the current through RL for the circuit of figure.
Norton’s Theorem Procedure

## Slide 9
Step 3:-Calculate RN by first setting all sources to zero (voltage sources are replaced by short circuits, and current sources by open circuits) and then finding the resultant resistance between the two marked terminals.
Norton’s Theorem
EXAMPLE 1: Find the Norton’s equivalent circuit. Then find the current through RL for the circuit of figure.
Norton’s Theorem Procedure

## Slide 10
Step 4:-Calculate IN by first returning all sources to their original position and finding the short-circuit current between the marked terminals.
Norton’s Theorem
EXAMPLE 1: Find the Norton’s equivalent circuit. Then find the current through RL for the circuit of figure.
Norton’s Theorem Procedure

## Slide 11
Step 4:-Calculate IN by first returning all sources to their original position and finding the short-circuit current between the marked terminals.
Norton’s Theorem
EXAMPLE 1: Find the Norton’s equivalent circuit. Then find the current through RL for the circuit of figure.
Norton’s Theorem Procedure

## Slide 12
Step 4:-Calculate IN by first returning all sources to their original position and finding the short-circuit current between the marked terminals.
Norton’s Theorem
EXAMPLE 1: Find the Norton’s equivalent circuit. Then find the current through RL for the circuit of figure.
Norton’s Theorem Procedure

## Slide 13
Step 4:-Calculate IN by first returning all sources to their original position and finding the short-circuit current between the marked terminals.
Norton’s Theorem
EXAMPLE 1: Find the Norton’s equivalent circuit. Then find the current through RL for the circuit of figure.
Norton’s Theorem Procedure

## Slide 14
Step 5:-Draw the Norton’s equivalent circuit with the portion of the circuit previously removed replaced between the terminals of the equivalent circuit.
Norton’s Theorem
EXAMPLE 1: Find the Norton’s equivalent circuit. Then find the current through RL for the circuit of figure.
Norton’s Theorem Procedure

## Slide 15
Norton’s Theorem
EXAMPLE 1: Find the Norton’s equivalent circuit. Then find the current through RL for the circuit of figure.
Converting the Norton equivalent circuit to a Thévenin equivalent circuit.

## Slide 16
Norton’s Theorem
EXAMPLE 1: Find the Norton’s equivalent circuit. Then find the current through RL for the circuit of figure.
Converting the Norton equivalent circuit to a Thévenin equivalent circuit.

## Slide 17
EXAMPLE 2: Find the Norton equivalent circuit for the network external to the 9 Ω resistor in Figure.
Norton’s Theorem

## Slide 18
Step 1 and 2:-
Solution:-
Norton’s Theorem
EXAMPLE 2: Find the Norton equivalent circuit for the network external to the 9 Ω resistor in Figure.

## Slide 19
Solution:-
Step 3:-
Norton’s Theorem
EXAMPLE 2: Find the Norton equivalent circuit for the network external to the 9 Ω resistor in Figure.

## Slide 20
Solution:-
Step 4:-
Norton’s Theorem
EXAMPLE 2: Find the Norton equivalent circuit for the network external to the 9 Ω resistor in Figure.

## Slide 21
Solution:-
Step 4:-
Norton’s Theorem
EXAMPLE 2: Find the Norton equivalent circuit for the network external to the 9 Ω resistor in Figure.

## Slide 22
Solution:-
Step 4:-
Norton’s Theorem
EXAMPLE 2: Find the Norton equivalent circuit for the network external to the 9 Ω resistor in Figure.

## Slide 23
Norton’s Theorem
EXAMPLE 2: Find the Norton equivalent circuit for the network external to the 9 Ω resistor in Figure.
Solution:-
Step 5:-
Or